## Slide 1: Drive-up Basics John Stroia President, Gunnebo North America and Hamilton Security

## Slide 2: Agenda
Introduction
Solution selling built around the branch
What’s happening with branches?
What’s happening with cash?
Drive-up 101
  Good Practices – “The Rules”
  Good Practices – Decisions
  Examples
The Hamilton Difference

## Slide 3: Solution Selling Built Around the Branch

## Slide 4: Number of Bank Branches of FDIC insured commercial Banks in US
77,647
82,425
21,122 CU
Branches
22,078 CU
Branches

## Slide 5: Volume of US Cash in Circulation

## Slide 6: Volume of US Cash in Circulation

## Slide 7: Why drive-up?
Overall convenience for customer
1.5 to 2 times more efficient than inside teller
Good alternative for low mobility customers
Can keep costly commercial transactions outside of branch
Supports American “drive-through/car” culture
Safer environment for tellers
Very convenient for parents

## Slide 8: Branch Design Basics
Branch/Drive-up drivers: Cars and Cash
Sight Location/Planning
Deal or no deal drawer
General design rule for small/regional banks and credit unions - 50-60% drive-up traffic and 40-50% walk-in traffic
Determining placement of drive-up on site
  Deal or no deal drawer (yes I said it again!)
    Pros – commercial and customer traffic
    Cons – limits branch design, one-to-one customer ratio, if you have it customers will almost ALWAYS pick the deal drawer first, commercial customers will have to wait.
  Important to separate drive-up traffic from inside teller traffic
  Ingress/Egress from street
Determine how commercial customers will be served
How the branch and drive-up are designed is a series of comprises and blending of sometimes conflicting strategies

## Slide 9: Drive-up Design Good Practices
Stacking four to five cars – 20’ per car
Good site lines – provide straight run; no severe turns

## Slide 10: Drive-up Design Good Practices
Min. eight foot lane width
Min. six inch curb heights
Min. 24 inch islands

## Slide 11: Drive-up Design Good Practices
Canopy as high as possible (will still get hit)
Bypass lane as wide as possible

## Slide 12: Drive-up Design Good Practices
Do not install other items in the lanes (gutters, spigots, electric/gas meters, venting, landscaping, etc.)
  Many of these items are NOT shown on elevations!
Have a plan for smoking and litter

## Slide 13: Drive-up Design Good Practices - Decisions
Type of drive-up – Attached, Reverse, Remote, Head-on, MotorBank
Determine ATM Location (first lane, island, other site location)
Determine how commercial customers will be served (Deal Drawer, Night Head, Commercial pneumatic lanes)
Overhead, underground or combination tubes
First lane pneumatic system
Wide lanes, higher height customer units

## Slide 14: Drive-up Design Good Practices - Decisions
Wide lanes, higher height customer units
Tandem lanes
Video – one or two-way (What does VAT stand for?)
Bollards
Local codes (design, stacking, noise, ingress/egress location, lighting, code study costs, etc.)
Bank security standards/cameras
Signage/Marketing
Open/Closed signs – Clearance Height signs – Labeling devices
Retrofit/Upgrade

## Slide 15: Drive-up Design – Head on

## Slide 16: Drive-up Design – Downsend Addition

## Slide 17: Drive-up Design - Remote

## Slide 18: Drive-up Design – Pneumatic in first lane

## Slide 19: Drive-up Design – Lane with LP Camera

## Slide 20: Drive-up Design – Examples

## Slide 21: Drive-up Design – Tandem Lanes

## Slide 22: Drive-up Design - IRT, Diverter

## Slide 23: Drive-up Design – First Lane Pneumatic

## Slide 24: Drive-up Design – Sharp Left Turn

## Slide 25: Drive-up Design – Poor Design

## Slide 26: Drive-up Design Good Practices - Decisions
Location of teller units
  Drive-up area
  Work room
  Front counter (Overhead or through-the-counter)
Teller Cash Recycler

## Slide 27: The Hamilton Difference
Broadest solution set
Built to Highest Standards

## Slide 28: Windows & Deal Drawers
Deal Drawers – The best in the industry….400DD & DCD18
  UL Level 3
  Patented suspension free design is far superior to competitors’ glides
  No “wind tunnel” effect
  Electric with manual option
  Optional Heater
  Adjustable to curb widths for customer
Windows
  UL Listed both the frame and glass
  UL Level 1, 2 or 3 glass
  Hurricane Approved
  5ft, 8ft, 10ft, 12ft, 15ft standard
  Custom sizes
400D
10ft with DCD18

## Slide 29
Hamilton Drive-Up Tube Systems
  Complete lineup
XLR – 4.5” Overhead
HA47 – 4”x7” Overhead
HA33 – 8” & 10” Overhead
XLRD – 4.5” Underground

## Slide 30: XLR - 4 ½” Drive-Up System
Built upon the legacy of the HA1000!
Both overhead and underground
Stainless Steel body – front and back
Top surround and base are ABS polymer
Service from the front
Two sets of call/send buttons
Integrated tubular design for two-way video
Improved location and housings of speaker and microphone  better audio quality
Optional Heater / Airflow kit (with thermostat)
No Truck Base needed……We will increase the overall height of the frame to accommodate extra height needed
Audio
console
Optional 2-way video

## Slide 31: HA47 & HA33
HA47 – Light Commercial Unit
  Can operate as both a retail and a commercial unit
  Transports 12 to 15 pounds
  4x7 type large carrier
  Blowers/motors inside customer unit
  Same control board as in HA33 and XLR
  2-way video can be added as an option
HA33 - Heavy duty commercial unit
  Available in both 8” and 10” units
  Transport up to 25lbs.
  Commercial system used for moving heavier items
  Captive Carrier
  Great for replacing Diebold 8”
  Blowers/motors mounted up in canopy or remote location
  Stainless Steel construction
  Optional 2-way video
HA33
HA47

## Slide 32: HA33

## Slide 33
Teller Terminal Options
Extended Teller with Stabilizer
Thru the counter
Downsend
Standard overhead
Wall mount bracket with clear tube
Double sided teller

## Slide 34: Drive-Up Options
15 inch two-way video
10 inch two-way video
License plate camera – now with IP/Analog
Diverter
Other Options…….
One way video
Teller mount brackets
Overhead conduit kit
Truck height XLR
Truck Base
Riser Plate
Add audio/video to competitors’ equipment

## Slide 35
Point to Point Systems
HT-15
HT-19

## Slide 36
    Designed to fit those units installed that need to be converted to a truck lane
    Part # XLR-ATB for upsend
    Part # XLRD-ATB for downsend
NEW HA-1000XLR Accessories
New Truck Base
Add-on Truck Base
NEW XLR-LED Light Kits for overhead HA1000-XLR to add some pizazz to drive-up.
Various color & flash pattern options
Remote controlled
Night lock mode
Available mid-Q3

## Slide 37
Coming
Soon!
Plus Anti-Bacterial Carriers

## Slide 38
XLR Riser Plate
Part# XLR-21K
Riser plate to cover footprint when replacing HA1000s & certain competitors’ equipment

## Slide 39
Teller Cash Recycler – Gunnebo TCR7
Gunnebo TCR7
Four Teller Installation

## Slide 40: TCR7 – New Design
UL-291 safe rating new rating w/ high tensile steel
New Muted Color Scheme
Reduced width by 3.7” from 20.7” to 17”
No Plastic vacuumed formed parts
10.1” touch screen, largest screen in the industry
Improved outer door locking mechanism
New design does not require any software changes
Can drive the coin dispenser
Serial number tracking on robbery dispense
Will hold 5 robbery dispenses
March Searchlight integration
Track and record TCR interactions
New cleaning cards and kits available
Power and data connection moved within the top cover

## Slide 41: Hamilton Activities
Webinars
Updating collateral
  Brochures
  Battlecards
  Drawings
Updated websites

## Slide 42
Thank you!
How can we help you to win business?